## Slide 1: Compiler Project Updates Nov 4th
Florida Institute of Cybersecurity Research Electrical and Computer Engineering Department
Arunabho Basu

## Slide 2: Progress at a glance
RISC-V Compiler Toolchain
RISC-V Compiler Addon
Physical Fault Modeling
Hardening Rules
GCC Cross Compiler built
Cross compiler turns C code to RISC-V executable
Targets bare-metal RISC-V core on QEMU emulator
Security hardening implemented through GCC add-on
Researching cross compiler stages and RV64I ISA
Physical Modeling of LFI
Memory mapping of faults
Assembler configuration
Hardening rules

## Slide 3: GCC RISC-V Cross Compiler Toolchain
riscv64-linux-gnu
  Targets Linux OS on RISC-V
  Lightweight embedded linux like petalinux preferred
riscv64-unknown-elf-gcc
  Targets bare-metal RISC-V
  Using qemu emulator to run riscv64 executables
  Yet to try it on actual riscv hardware
Another notable riscv cross compiler project
  xPack riscv-none-elf-gcc
  https://github.com/xpack-dev-tools/riscv-none-elf-gcc-xpack/releases/tag/v14.2.0-2
  Questions about hardware in use

## Slide 4: RISC-V compilation
Pre-processing
  Replaces macros and includes header files, resulting in a pure C source file with no preprocessor directives.
  riscv64-unknown-elf-gcc -E fics.c -o fics.i
Compilation
  Translates the preprocessed C code into assembly code for the RISC-V architecture
  riscv64-unknown-elf-gcc -S fics.i -o fics.s
Assembly
  Converts the assembly code into machine code, resulting in an object file
  riscv64-unknown-elf-as fics.s -o fics.o
Linking
  combines one or more object files (and any required libraries) into a final executable file
  riscv64-unknown-elf-gcc fics.o -o fics

## Slide 5: RV64I - Extensions
Unique feature of RISCV ISA – Base ISA can be expanded using extensions
Extensions can be customized for suitable use cases
There is a possibility of using extensions to implement hardening[1]
Hardened RISCV ISA
In this case compiler would not compile to base RISCV ISA, it will compile to hardened RISCV ISA [1] XuanTie VirtualZone: RISC-V-based Security Extensions | Xuan Jian, Alibaba Cloud https://riscv.org/blog/2022/04/xuantie-virtualzone-risc-v-based-security-extensions-xuan-jian-alibaba/

## Slide 6: RISCV Extension Table

## Slide 7: RISCV Extension Downside
Special Instruction Set – requires Special Hardware!
Custom RISCV core needed
Compatibility issues expected

## Slide 8: Research Direction Question
Implement hardening :
  In the Instruction Set itself?
  OR
  Compiler Addon?

## Slide 9: Physical Fault Modelling
Existing GCC Options
Compile time Options
Run time Options
Control Flow Options
Stack Hardening
Function hardening
Jump statement hardening
Loop Hardening
Pointer Hardening
FI/SCA model vectors
FI
  Laser
  Clock
  Voltage
SCA
  EM Wave
  Power
  Time
Attacks which can be detected/prevented by these options

## Slide 10: THANK YOU