## Slide 1: Compiler Project Updates May 12
Florida Institute of Cybersecurity Research Electrical and Computer Engineering Department
Arunabho Basu

## Slide 2: Overview
  Objective : Secure Software Execution by implementing Physical Hardening during Compilation stage
  Current objective : Proof-of-concept Example of Physical Hardening
          Hardening against conditional branch instruction skipping
          Fault Injection Analysis using SoFi to quantify the improvement made by Hardening
  Harden
  What happened during hardening ?
  Faults modifying/bypassing branch condition will now directly lead to password checking failure instead of secret asset
  Approach : Simple program wrote in C and compiled using C to RISCV cross compiler.
  Compiled program co-simulated over PicoRV32 soft core.
  The program counter is used to locate target instruction for Fault Injection and then SoFi is used for FIA.

## Slide 3: Fault Injection – Locating the Fault
  Targeting the unsafe branch instruction for Fault Injection
password.elf
Compile with C -> RISCV cross compiler
Add start.elf, and convert all to firmware32.hex
RTL simulation in VCS
picorv32.v with firmware32.hex onboard memory

## Slide 4: Fault Injection – Locating the Fault
  Dumped PC values – physical addresses
  Looked up machine code in firmware at corresponding addresses
  Disassembled and decoded machine code
  Executed in recursive fashion to get all instructions disassembled
  Locate target register and cycle during simulation
  reg_pc[31:0] – Program Counter
  Automated using Python scripts

## Slide 5: Fault Injection – Locating the Fault
  Disassembled Firmware
  Almost 800 branching instructions alone
  Disassembled Firmware
  Assembly Code before Linking
  Fault Target : 0001603c: 02050063 beqz a0,1605c <main+0x68>

## Slide 6: Fault Injection – Locating the Fault
  Fault Target : 0001603c: 02050063 beqz a0,1605c <main+0x68>
  Fault Target Cycle : 81560000 ps
  sff_gen.py script to create Fault List for Z01X
  Design Netlist + Fault Location +
  Fault Cycle + Fault Type

## Slide 7: Security Properties
  Implemented as Strove File
  Security Property to detect skipping BEQ instruction
  Fetch opcode at same location between Good Machine (GM) and Faulty Machine (FM)
  If they differ, instruction was skipped or corrupted

## Slide 8: Current Progress
  Synthesize design to netlist file so it works with SoFi
    Henian’s suggestion : use 32nm standard library and Cadence Genus for synthesis
  Use sff_gen.py to create Fault List in a way it works with SoFi
    Henian’s suggestion : split large fault list to segments so it doesn’t crash and take whole day
  Make sure Fault List, Security Properties and Design are aligned in timing cycles
  Run SoFi toolchain to do Fault Injection Analysis -> Quantify Impact of Hardening Technique

## Slide 9: Upcoming SRC Deliverables
  KPI Form
    Deadline : June 26
    On track to be completed by May 15 for advisor’s review
  GRC Poster Presentation (June 3-4, UT Dallas)
    Deadline : May 20
    On track to be completed by May 15 for Dr Rakib’s and advisor’s review
  Annual Review Presentation
    Deadline : June 26
    Early first draft completed and being reviewed by Dr Rakib, more content would be added over next few weeks
  Summer Deliverables as per SRC Website

## Slide 10: Upcoming SRC Deliverables
  June 30 Deliverable
  The timeline of project is presented intuitively in a step-by-step way but not aligned well with our development plan
  There is a primary disconnect between proposed plan of tasks and actual plan which would affect our very first quarter deliverable
  Summer Deliverables as per SRC Website

## Slide 11: Project Tasks and Timeline
  Proposed Timeline and Deliverables
    Year 1 : Task 1
      FIA Modeling
      SCA Modeling
      Attack Model Fine Tuning
    Year 2 : Task 2
      Compiler Development
      Define Security Properties & develop Hardening Rules
      Scaling Hardening Database
    Year 3 : Task 3
      Evaluation and debugging
      Test and Demo on physical chips
  Actual Development Plan
  Year 1 : Task 1 and Task 2
    FIA Modeling
    Compiler Development
    Attack Model Fine Tuning
  Year 2 : Task 1 and Task 2
    SCA Modeling
    Compiler Development
    Scaling Hardening Database
  Year 3 : Task 3
    Evaluation and Debugging
    Test and Demo on physical chips

## Slide 12: Proposed Project Tasks and Timeline
Task 1: Attack Modeling
Task 2: Compiler Development
Task 3: Evaluation
  Which of the following should we do ?
    Strictly follow the timeline, meaning that it's better we all put the major effort on SCA modeling now, and stop the compiler hardening effort since it's part of 2026 plan.
    Doing it as the currently way, which is working on modeling, hardening in parallel. Then should we adjust the timeline to do SCA modeling at later years?

## Slide 13: THANK YOU

## Slide 14: Conditional Branch Hardening
  What happened during hardening ?
  Faults modifying/bypassing branch condition will now directly lead to password checking failure instead of secret asset
  Hardening implemented by Static Branch Prediction Hint : __builtin_expect(branch condition, 0)
  Harden
  Security Property : Default fall-through branch handles error rather than security asset

## Slide 15
Next step – Evaluation of Hardening
  Targeting the unsafe branch instruction for Fault Injection
password.elf
Compile with C -> RISCV cross compiler
Add start.elf, and convert all to firmware32.hex
RTL simulation in VCS
picorv32.v with firmware32.hex onboard memory

## Slide 16
Analyzing the waveform to find target signal
:
d
r
o
_
I
n
c
o
Output buffer containing register goes from “Input Password: ” to “Incorrect Password”
Expanding to look at instructions in program counter around this time
Looking up the instruction at the particular memory location and disassembling it

## Slide 17
  Disassembled machine code don’t match high level unlinked assembly code
Current roadblock
assemble + link
disassemble + unlink
High level assembly code before
Disassembled code from firmware

## Slide 18
  Disassembled machine code don’t match high level unlinked assembly code
Current roadblock
  What’s possibly happening here :
  Assembly to Machine is 1 to 1 but not the other way around ( example: MOV AX, BX and MOV AX, BX might compile to the same machine code as another mnemonic if the assembler allows aliases or if different syntaxes exist. )
  Assembler optimizations and pseudo instructions ( example: NOP could be represented as MOV EAX, EAX or an actual 0x90 byte depending on context or architecture)
  Different disassembler behavior based on target architecture, endian-ness
  Assembler and Disassembler Pair Mismatch (Intel vs AT&T)
  Unaligned Machine Code

## Slide 19
  Evaluating the Hardening :
  Mapping disassembled code to assembly code
  Analyzing the waves to find targets that will impact critical instruction
  Fault injection simulation using SoFi
Next steps

## Slide 20: [Henian Slide] Locate Critical Assembly Code Snippets
Given several lines of critical C/C++, how do we determine
  What part of assembly codes are generated from them?
  When are these assembly instructions executed in hardware
  What hardware resources these instructions are using? -> can be done by checking switching activities during a certain time window (still need to know the window first)
GDB built in riscv-gcc cross compiler does not come with this feature
  The gcc-riscv cross compiler should be re-built with “—enable -tui” flag to support
  Looking for the possibility to install this library
  On the other hand, micro-architecture level fault simulators might have solved this issue
An example of using GDB debugger to locate specific assembly instructions

## Slide 21: Progress at a glance
  Making decent progress, on track to meet first quarter deliverables
    Deliverables : 1) SRC first quarter report by April **
            **Need access to SRC project on pillar science website
  Detailed analysis of GCC compiler introduced vulnerability and its corresponding hardening
    How Branch Prediction Optimization makes code more vulnerable to LFI
  Shared reading materials with Mashahed and bringing him upto speed on the project
  Making the toolflow setup accessible to Pantha and Mashahed so we can work together

## Slide 22: Conditional Branch Hardening
  What happened during hardening ?
  Faults modifying/bypassing branch condition will now directly lead to password checking failure instead of secret asset
  Hardening implemented by Static Branch Prediction Hint : __builtin_expect(branch condition, 0)
  Harden
  Security Property : Default fall-through branch handles error rather than security asset

## Slide 23
  Dumped all internal states of compilation and studied how compilation takes place.
  $ riscv32-unknown-elf-gcc -fdump-tree-original password.c –c
  $ riscv32-unknown-elf-gcc -fdump-tree-gimple password.c –c
  $ riscv32-unknown-elf-gcc -fdump-tree-all password.c –c
  $ riscv32-unknown-elf-gcc -O2 -fdump-tree-cfg-graph -c password.c

## Slide 24
  Before and After Branch Prediction Optimization
  $ riscv32-unknown-elf-gcc -O2 -save-temps password.c -o password
  $ riscv32-unknown-elf-gcc -O1 -save-temps password.c -o password
  Branch Prediction Optimization switched the default branch
  Before
  After
  High level code had error in default branch (else)

## Slide 25: Branch Prediction Optimization
  How does this optimization help?
  Optimization : Hot Branch Instructions clustered together and pre-loaded into instruction cache pipeline so they can be readily fetched if condition is met
    If branch condition is met next instruction is already in pipeline (saves time)
    If branch condition is not met pipeline is flushed and cold branch is loaded (takes more time)
Branch Prediction Optimization
  Hot Branch
  Most likely taken branch based on analysis
  Cold Branch
  Less likely taken branch based on analysis

## Slide 26
Hot Branch
Cold Branch
Branch Condition
Instruction Cache Pipeline
  How does this optimization help?
  Optimization : Hot Branch Instructions clustered together and pre-loaded into instruction cache pipeline so they can be readily fetched if condition is met
    If branch condition is met next instruction is already in pipeline (saves time)
    If branch condition is not met pipeline is flushed and cold branch is loaded (takes more time)
Branch Prediction Optimization

## Slide 27
Access to Secret Asset (Hot Branch)
Error Handling (Cold Branch)
Branch Condition
Instruction Cache Pipeline
  How does this introduce Fault Injection Vulnerability ?
  - Faults modifying/bypassing branch condition will now directly lead to secret asset
Branch Prediction Optimization - Vulnerability

## Slide 28
  Vulnerability :
  Branch Predictor does not know if a branch has security asset and should be kept cold
  Branch Predictor decides hot (most likely) or cold (less likely) based on heuristic analysis
    Heuristic Analysis – detect error handling code, assign it cold always
Branch Prediction Optimization - Vulnerability
  Standard GCC compiler in default setting would always assign error handling branch as cold even if other branch has security asset

## Slide 29
  Hardening :
  Simple naïve solution : Turn off Branch Prediction Optimization
  Advanced solution : If there is a security asset, assign it always cold
    Static Branch Prediction Hint : __builtin_expect(branch condition, 0)
    Profile guided Optimization (Dynamic) : Branch Prediction is guided by a profile containing branch weights (customizable)
Branch Prediction Optimization - Hardening
  Security Property Hardened : Default fall-through branch handles error rather than security asset

## Slide 30
  Evaluating the Hardening :
  Impact on performance – time taken and resources used measured before and after hardening
  Impact on Fault Injection Resilience – measured using SoFI before and after hardening
Next step – Evaluation of Hardening

## Slide 31
  Evaluating the Hardening :
  Impact on performance – time taken and resources used measured before and after hardening
    Time measured showed negligible overhead
    Possible reasons : short and lightweight program, maybe parallel processing was involved(?)
    Performance measured using perf : slightly increased cache-miss because now security asset needs to be loaded from cold branch
    Next step : evaluate other heavier programs
  Impact on Fault Injection Resilience – measured using SoFI before and after hardening
    Working with Pantha to troubleshoot SoFI
Next step – Evaluating Performance

## Slide 32: Next steps – Evaluating Fault Resiliency
  Input – Design File, Security Properties File, Fault List
  Output – Fault Assessment
  Analyze the waveforms to identify LFI target signals
  LFI Target list used to generate : - security properties and - hardening rules
  PicoRV32 CPU with test program loaded into memory
  Co-simulation using suitable Verilog simulator
SoFI Framework
  Quantified hardening analysis and report
  PicoRISC-V CPU
  Verilog softcore
  RV32i ISA
  Test program (for FIA)
  Runs on RISCV (written in C, compiled using riscv cross compiler)
  Compiled code converted to 32bit firmware in hex format

## Slide 33: The issues with SoFI
SoFI Framework
  Quantified fault resiliency report
  INPUT 2 : Critical Locations/Fault list
  Identifying critical locations from waveform analysis – local fault targeting our security property or global faults?
  INPUT 3 : Security Properties File
  Defining security property in a way SoFI can understand. Henian suggested editing his file but I am not sure if its working
  INPUT 1 : Design File
  Henian’s work show gate level netlist of design is accepted. Our RTL level design was synthesized to Gate level netlist.
  The synthesis process directly impacts the physical modelling of faults

## Slide 34: Current Framework
  PicoRISC-V CPU
  Verilog softcore
  RV32i ISA
  Test program (for FIA)
  Runs on RISCV (written in C, compiled using riscv cross compiler)
  Compiled code converted to 32bit firmware in hex format
  Firmware loaded on to memory of CPU core
  PicoRV32 CPU with test program loaded into memory

## Slide 35: Current Framework
  Input – Design File, Security Properties File, Fault List
  Output – Fault Assessment
  Analyze the waveforms to identify LFI target signals
  LFI Target list used to generate : - security properties and - hardening rules
  PicoRV32 CPU with test program loaded into memory
  Co-simulation using suitable Verilog simulator
SoFI Framework
  Quantified hardening analysis and report

## Slide 36: Current Roadblock
  Analyze the waveforms to identify LFI target signals
  PicoRV32 CPU with test program loaded into memory
  Co-simulation using suitable Verilog simulator

## Slide 37: Current Roadblock
  Analyze the waveforms to identify LFI target signals
  PicoRV32 CPU with test program loaded into memory
  Co-simulation using suitable Verilog simulator
Simulation using Iverilog
Simulation using VCS
vs
Example (using Hello World):

## Slide 38: Troubleshooting update
  What we know :
  VCS not cosimulating it correctly
  Not an issue with machine – same error reproduced on Henian’s machine
  Not an issue with test program code, all programs cosimulated on VCS giving erranous results while its working on iverilog
What we’re trying :
- Troubleshooting using error codes
- Checking VCS options from man page
- Modifying testbench
- Check other simulators
Simulation using Iverilog
Simulation using VCS
Another Example (using AES):

## Slide 39: Current Progress
Reading up on SoFI tool and how to use it
Researching FIA Vulnerability Analysis :
  Features/Characteristics that help in quantifying hardening
  Features that help in improving physical attack model
  Features whose impact can be augmented by compiler level hardening
Reading up on LFI and Physical Modeling

## Slide 40: Next Steps
Identifying Critical Instructions/Locations
Developing a framework that can identify critical instructions in code
Identifying hardening technique – replacement/addition/rewriting
  which gives positive change in hardening metrics,
  while keeping overhead low, and
  implementable during compilation stage

## Slide 41: Hardening example
Develop a GCC plugin that takes the non-hardened version and hardens it
Very similar approach to linting software
Required : Clear understanding of pre-processing stage and compilation stage of gcc-riscv32 compiler – how source code is translated to riscv instruction
Other hardening rules?

## Slide 42: Objective 1 – Compiler Toolchain
Architecture in use : RISC-V
Core in use : PicoRV32
GCC Cross-Compiler toolchain : gcc-riscv32-unknown-elf
Current Tasks :
  Getting familiar with RISC-V ISA and the GCC cross compiler toolchain
  Have started compiling simple programs to better understand pre-processing and compiling stage
  Goal is :
    Compile an AES program with a LFI vulnerable instruction
    Develop a plugin that hardens the said instruction

## Slide 43: Physical Fault Modelling
Existing GCC Options
Compile time Options
Run time Options
Control Flow Options
Stack Hardening
Function hardening
Jump statement hardening
Loop Hardening
Pointer Hardening
FI/SCA model vectors
FI
  Laser
  Clock
  Voltage
SCA
  EM Wave
  Power
  Time
Attacks which can be detected/prevented by these options

## Slide 44: Challenges in security Hardening
Hardening Toolflow :
  Identify and locate critical instructions, vulnerable to fault injection
  Harden the critical instruction
Going from C code to RV32i assembly code, locating critical instruction is not very straightforward
Pre-silicon vs Post-silicon
  RTL simulation cycle varies from actual hardware implementation cycle – making finding exact cycle even harder

## Slide 45: Security Hardening Example
Henian’s example of a simpler testcase: password authentication
  Call secret function under the correct key input
  What if “bnez a0, .L1” is skipped?
compile

## Slide 46: PicoRV32 Core
PicoRV32 is a Verilog softcore
Simulated on local machine and the compiled code is co-simulated on top of the softcore by inserting it into the memory of PicoRV32

## Slide 47: RISC-V compilation
Pre-processing
  Replaces macros and includes header files, resulting in a pure C source file with no preprocessor directives.
  riscv32-unknown-elf-gcc -E fics.c -o fics.i
Compilation
  Translates the preprocessed C code into assembly code for the RISC-V architecture
  riscv32-unknown-elf-gcc -S fics.i -o fics.s
Assembly
  Converts the assembly code into machine code, resulting in an object file
  riscv32-unknown-elf-as fics.s -o fics.o
Linking
  combines one or more object files (and any required libraries) into a final executable file
  riscv32-unknown-elf-gcc fics.o -o fics
GCC Cross Compiler
C Code
Compiled RV32i code

## Slide 48: Compiler Project Updates Feb 3rd
Florida Institute of Cybersecurity Research Electrical and Computer Engineering Department
Arunabho Basu

## Slide 49: Security Hardening Example
Example of a simple testcase: password authentication
  Call secret function under the correct key input
  What if “bne a0, zero, .L3” is skipped?
compile
  PC falls through to next sequential address which is the secret

## Slide 50: Security Hardening Example
harden
  What if “beq a0, zero, .L3” is skipped?
  PC can never reach branch L3 containing Secret Function

## Slide 51: High Level Analogy
Inequality Check
Equality Check
Same operation implemented in two ways :
  High level logic:
  If passwords don’t match
    Jump to Error
  Default (else) : Access Secret
  High level logic:
  If passwords match
    Jump to Access Secret
  Default (else) : Error

## Slide 52: Attacker’s Perspective
  Attacker’s Goal : Skip bne instruction
  Result : PC falls through to secret branch
  Attacker’s Goal : Make beq instruction always true
  Result : PC jumps to secret branch

## Slide 53: Primary LFI Target
Comparator Is a0 == 0 ?
Branch Target Address
Next Sequential Address
Final PC
MUX PC Decision
Final PC
Comparator Is a0 != 0 ?
Branch Target Address
Next Sequential Address
MUX PC Decision
Secret
Secret
Error
Error
Branch Condition
Branch Condition
OR
OR
a0
a0

## Slide 54: Other LFI Targets – Harder to Exploit
Register File: If the attacker can flip the value in a0 from nonzero to zero, then the branch condition changes. (Harder to flip because of small time window)
Instruction Decoder: A fault might corrupt the bne instruction opcode itself, turning it into a no-op or an always-jump. (Multiple Faults + Very hard to flip to target opcode)
Pipeline Latches/Flip-Flops: The pipeline stage registers store intermediate signals—if you flip the stored comparator result or the branch target PC, you can misdirect control flow. (Multiple Faults + Very hard to flip to target address)
PC Increment Logic: Even if the comparator is correct, messing with the final PC increment or branch addition could skip or misalign instructions. (Multiple Fault + Hard to locate)

## Slide 55: Quantifying Hardening
Hardening Metric = 2-1
Non-Hardened Assembly Code
FIA Vulnerability Analysis (1)
SoFI
Hardened Assembly Code
FIA Vulnerability Analysis (2)
SoFI

## Slide 56: SoFi Fault Analysis – Current Progress and Challenges
Current Progress – Troubleshooting SoFI RTL Implementation
SoFI Input :
  RTL Design File –
    Co-simulation of softcore RISC-V and non hardened program executable
    Generates VCD file of simulation from VCS
    Challenge – Timing and memory mapping the co-simulation
  Stimulus VCD File –
    ZO1X simulation to find faults that violate SP
  Security Property File (Strobe File) –
    No instruction skipping
    Challenge – Locating the fault cycle

## Slide 57: SRC Proposal Deliverables and Timeline
Quarter 1-3 : SPICE-level and layout-level modeling of the physical characteristics of fault injection and side-channel attacks
Quarter 4 : Post-silicon attack test on chip/SoC, perform vulnerability analysis of software executions, and improve the attack models.
Quarter 1 : Investigation and development of physically-aware hardening techniques
Quarter 2 : Developing executable security properties and LUT/ML-based model interfaces to guide hardening strategies.
Quarter 3-4 : Integration of hardening techniques into software compilation in the form of GCC plug-in/LLVM/Clang
Quarter 1-2 : Extensive validation of the PASS flow on FPGA platform with iterative test of hardened software compilations
Quarter 3-4 : Broadening the attack scenarios by including more security properties, and fine-tuning of physical attack models.
Year 1
Year 2
Year 3

## Slide 58: SRC Proposal Deliverables – Year 1 (2025)
Qtr 1
Qtr 2
Qtr 3
Qtr 4
FIA Modeling : SPICE Level
FIA Modeling : Layout Level
SCA Modeling : SPICE Level
SCA Modeling : Layout Level
Post Silicon Attack Test
Vulnerability Analysis of Software Execution
Improve Attack Models

## Slide 59: SRC Proposal Deliverables – Quarter 1 (March 2025)
Qtr 1
Fault Injection Modeling – SPICE Level
Set up RTL design files
Set up Testbench
Run Transient simulations
Model and inject fault during transient simulations
Harden and repeat last step
Evaluate difference between before and after

## Slide 60: THANK YOU