## Slide 1: Florida Institute for Cybersecurity Research FIA Update: Physical Modeling
Pantha Protim Sarker
11/04/2024

## Slide 2: Direction from Last Meeting
      Goal:
        ML based physical modeling for Fault Injection analysis
      Task 1:
        Physical modeling of Laser Fault injection
      Paper
        GOMACTech: Two-page abstract submitted, full paper work in progress
        HOST: ML based EMFI analysis, currently working with Ansys team.

## Slide 3
Problem Definition
Developing an end-to-end approach for fault injection vulnerability assessment based on physical modeling
Fault can be single fault or multi fault
Developing a vulnerability assessment metrics
Should consider the effect of technology node sizing, and CAD library
Develop a ML based assessment
Research Questions
Can the modeling assessment be independent of the attack modalities (Ex.: Laser, Flash gun, EM coils etc.)?
Can larger sized gates in a security critical location (from SOFI) be an effective countermeasure without affecting the performance and overhead?
From gate level to layout level, increasing gate sizing will lead to optimization problem. How to optimize the place and route?
ML Based Physical Modeling of Fault Injection

## Slide 4
Fault Injection Attacks Overview
Fault Injection Attacks
Voltage Glitch
Clock Glitch
EMFI
Laser
Optical
V Depletion: increases delay in wire
V Spike: setup time violation
Period Decrease: Setup/hold time violation
Inducing Eddy Current
Focused Beam:
Transistor states change due to current flow
Focused Beam:
Transistor states change due to current flow

## Slide 5
Laser Fault Injection
Fault Injection Modalities

## Slide 6: Optical Fault Injection
Optical fault injection preliminaries
Backside
  Si bulk is transparent to ~1050-1300 nm
  Which is near infrared region
  Visible light wavelength 380-700 nm
  Optical sources (other than near infrared laser) will not penetrate the bulk Si.
  No high energy near infrared source(other than the laser source) is available.
Frontside
  High power flashgun available in the market
  Literature review: older technology node
    350 nm technology
    EEPROM, Flash memory
    Latest 130 nm custom chip (Latest paper 2016)
Si Substrate
Active region
Visible light
Si Substrate
Active region
Visible light
Metal Layers

## Slide 7
EM Fault Injection
Eddy current on the PG grid

## Slide 8
Fault Injection Attacks Overview
Fault Injection Attacks
Voltage Glitch
Clock Glitch
EMFI
Laser
Optical
Focused Beam: Photocurrent
Radiation and focused beam: Induced Current?

## Slide 9
Threat Model and Assumptions
An adversary’s objective is to tamper with security-critical locations and violate security properties
Grey box attack model
Require physical access to the target device
Non-invasive or semi-invasive(backside polishing) fault injection
Attacker has access to certain optical/opto-electrical setup-
  Laser source, ex: Diode laser
  Optical source, ex: Flash gun
  XYZ stand for precise placement
  Measurement tools, ex: PC, oscilloscope etc.
Threat Model for Optical/Laser Fault Injection

## Slide 10
Laser Fault Injection
Fault Injection Modalities

## Slide 11: Electrical Modeling of the Laser
a,b – Are the parameters related to laser Power.
; Is the bivariant distribution of laser beam. Dependent on the lenses.
Pulse – Is the laser pulse width
S – Area of the p-n junction.
Laser power (1000 mW – 5000 mW) 45 nm Tech node
Iph-peak ~ (144 uA-600 uA)

## Slide 12: Spice Simulation of Standard Cells
Laser sensitive region for output state 0 ->1
Laser sensitive region for output state 0 ->1
Inverter

## Slide 13: Standard Cell Simulation
Standard Cell | Iph Threshold (0  1) (uA) for Gate Size of 120nm (X1) | Iph Threshold (0  1) (uA) for Gate Size of 240 nm (X2) | Iph Threshold (0  1) (uA) for Gate Size of 480nm (X4)
Inverter | 57 | 120 | 227
Nand2x1 | 84 | 178 | 325
And2x1 | 81 | 163 | 313
Nor2x1 | 63 | 137 | 250
Or2x1 | 77 | 144 | 309
Xor2x1 | 88 | 164 | 345
Xnor2x1 | 86 | 172 | 332
AOI21x1 | 98 | 208 | 392
OAI21x1 | 101 | 199 | 412
AO21x1 | 97 | 190 | 368
DFF | 144 | 224 | 374
Spice simulation for 45 nm tech mode during pull-up