## Slide 1: GCC-RISCV Compilation
Finally built the PicoRV32 core
Simulated assembly instructions on PicoRV32
  Built the GCC-riscv compiler tool chain
  Now this flow fully support taking any source code input, compile, and co-simulate with hardware at RTL
Compile – Assemble – Link process
  Compile: software -> assembly
  Assemble: assembly -> binary
    To turn .S to machine code specifically for PicoRV32, we need to allocate the address of instr. mem, reg. file, etc.
  Link: binary -> executable
    GCC-riscv will link to Newlib, which does not have a static entry point of program (not supported by PicoRV32)
    Addressed this issue.
Add a flag here to turn on any build-in or customized hardening technique, e.g.:
-fplugin=./security_plugin.so
ELF is a cross-platform binary format supporting many CPUs or ISAs
start.S initiates registers and the stack
Flow automated in Makefile

## Slide 2: Simulation Results from AES Software
Using a popular AES implementation in C from Github
Simply run the compiled executable
aes.elf or
aes.exe
compile
Add start.elf, and convert all to .hex
RTL simulation in VCS

## Slide 3: Hardening Compilation
However, even this simple AES has 66,797 lines of assembly instructions (in RISC-V)
  Learning GDB (GNU debugger)’s code tracking feature to get a C-assembly mapping
A simpler testcase: password authentication
  Call secret function under the correct key input
  What if “bne a0, zero, .L3” is skipped?
compile

## Slide 4: Hardening Compilation
Built-in GCC hardening flags did not solve this.
  Canary-based stack overflow protection is added
Same vulnerability here
harden

## Slide 5: Locate Critical Assembly Code Snippets
Given several lines of critical C/C++, how do we determine
  What part of assembly codes are generated from them?
  When are these assembly instructions executed in hardware
  What hardware resources these instructions are using? -> can be done by checking switching activities during a certain time window (still need to know the window first)
GDB built in riscv-gcc cross compiler does not come with this feature
  The gcc-riscv cross compiler should be re-built with “—enable -tui” flag to support
  Looking for the possibility to install this library
  On the other hand, micro-architecture level fault simulators might have solved this issue
An example of using GDB debugger to locate specific assembly instructions

## Slide 6: A Simple Example of Hardened Code
We can now compile any C/C++ code for RISC-V, and simulate in RTL with PicoRV32 core
Next
  Improve, automate, and add this feature into GCC plug-in
  To verify the effectiveness of this hardening, first, we need to find the exact cycle(s) when executing specific instruction lines in RTL simulation
harden
  What if “beq a0, zero, .L3” is skipped? Still safe.