## Slide 1: Taxonomy for Software Hardening Scenarios against Physical Attacks
General idea: model, attack, harden
Model – classified by abstraction levels
  Instruction-level model: bit-flip on instructions (already in literature)
  Microarchitecture-level model: bit-flip on microarchitecture components (already in literature)
  RTL / gate-level model
  Layout-level model
Attack (security analysis) – classified by abstraction levels
  RTL / gate-level fault simulations
  SPICE / Layout level simulations
  Post-silicon attacks
Harden – classified by dependencies on design details
  White-, grey- or black-box attacks

## Slide 2: Taxonomy for Software Hardening Scenarios against Physical Attacks
 | Model | Attack | Harden | Pros | Cons
Previously discussed Pre-silicon flow | RTL/gate-level model: For FIA: bit-flips, considering: the fault duration, timing in terms of cycles; the fault type in terms of global / local faults; the fault locations in terms of the number of concurrent faults For SCA: early design-stage power/EM/optical model Layout-level model: For FIA: Analog variations (e.g., current or delay), once a threshold or reference value is given, the analog variations could indicate a fault's feasibility. Currently we could model laser's direct impact (Iph), and we can work on modeling laser-induced local IR drop (Iph_sub). For SCA: cell-level pin current | For FIA and SCAs: Fault simulations at RTL/gate-level For LFI and SCAs: Layout-level simulations All simulations need security properties to determine whether the software is secure | White or black box? From software to RTL, gate-level, and layout, what stages do the hardening techniques have a dependency on? The answer depends on what levels of models' info we used to guide hardening. E.g., if we determine instructions' vulnerability levels only based on their corresponding hardware resources' cell type, size, and lib. Then it's more of a grey-box protection. | Using physical info to harden compilations is very innovative; Easier to operate -- we have multiple flows available including SoFI, LFI simulation flow at layout level, SCA flow, etc. | Implementing grey and black box hardening techniques could be challenging; The effectiveness of the hardening techniques are questionable if without post-silicon validations.

## Slide 3: Taxonomy for Software Hardening Scenarios against Physical Attacks
 | Model | Attack | Harden | Pros | Cons
Previously discussed Post-silicon flow | Establish the models from post-silicon results. | Post-silicon attacks for validation-purpose and help improve the attack models. We also need security properties, but they are checked by manual observations instead, to determine whether the software running is secure. | Two scenarios: 1. we know the design, and we build the models with the knowledge dependent on the design. We exploit these models to guide our hardening. Then it's a white-box hardening. 2. we did not use any models, we just try out every hardening technique we have on the software, run the attacks again and check the results and overhead. In this case, although our final protections are concluded from one single design (so its effectiveness may depend on this design), it's more of a grey- or black box hardening. The drawback of only testing on one design could be eliminated if we setup a "secure software testchip collection" | It's more like a "physical test lab for secure software", if the lab flows and guidelines are settled, it's fast and easy to adopt. | Time and equipment cost to setup the test. We need to successfully perform all intended attacks first and get experienced. Post-silicon modeling seems difficult, we do not have a plan on how to achieve this yet.

## Slide 4: Taxonomy for Software Hardening Scenarios against Physical Attacks
 | Model | Attack | Harden | Pros | Cons
SRC proposal: a combined flow | RTL/gate-level, and layout-level models are the same as in pre-silicon flow But we also proposed the models could be improved from post-silicon attack results. | We prioritize using post-silicon attacks for validation-purpose and also help improve the attack models. We didn't emphasize the RTL/gate-level and layout simulations. | white-box | Discussed in previous forms | Discussed in previous forms

## Slide 5: Reflections
All combinations of Model, Hardening, Attack levels could potentially work
  Pre-silicon model + post-silicon attack
  Post-silicon model + pre-silicon attack (simulations)
Hardening
  The hardening always happen on instructions. E.g., instruction duplications, reorganizations of conditional branches, loop hardening, strategically avoiding specific instructions
  Black or white box？
  How and how much hardening uses the info from modeling
  What user-specific scenario a flow is designed for