## Slide 1: Physically-Aware Secure Software Execution
Mark Tehranipoor
Chair, ECE Department, Intel Charles E. Young Endowed Chair Professor at University of Florida, Founder, Caspia Technologies

## Slide 2: Problem Statement
Problem: Protect assets
  On-device keys (crypto/obfuscation)
  Manufacturer firmware
  Application software
  On-device sensitive data, etc.
Software running on vulnerable circuits are not secure
  Software executed in SoCs, processors, IoT devices, and smartphones is susceptible to both cyber attacks and hardware attacks
  Physical attack targets the implementations, bypassing upper-level protections; it’s a powerful attack type compromising the confidentiality, integrity, and availability of modern chips
Software developers/compilers are not informed of physical attacks (fault injection, side channel, data extraction, etc.)
  The only existing physical modeling in compilers is based on unrealistic software-based predictions
Source: Intel

## Slide 3: Problem Statement
A Simple Example to Motivate the Work:
The faulty behavior in many different types of RISC-V instruction shows a powerful potential for attackers to manipulate the program execution
Notes: Faults marked with a number are complex/combined faults, explained in reference paper 5.

## Slide 4: Problem Statement
Physical Attacks
  Fault-injection attack (FIA)
    Clock/voltage glitching, laser/optical fault-injections, EM fault-injection
  Side-channel attack (SCA)
    Leakages from power, EM, optical, thermal, acoustic, etc.
    Can be monitored and analyzed to leak sensitive info
Illustration of different physical fault injection attacks
Side channel attack flow

## Slide 5: Motivations and Goals
Motivations
  Addressing physical threats from code compilation is fast, powerful, scalable, and cost-effective
  Existing physical modeling in compilers is on based on software-side predictions
Objectives
  The objective is to harden the software code against as many physical vulnerabilities as possible at the compilation stage.
  Effective physical modeling to help improve the compilation process
  Making code resistant to physical attacks at compilation stage
Software Hardening against Physical Attacks at Compilation

## Slide 6: Project Tasks and Timeline
Task 1: Attack Modeling
Task 2: Compiler Development
Task 3: Evaluation
 | Year 1 |  | Year 2 | 
Task 1: Attack Modeling |  |  |  | 
Task 2: Compiler Development |  |  |  | 
Task 3: Evaluation |  |  |  | 

## Slide 7: Task 1: FIA/SCA Modeling
Technical Approach
  Understand the logical impact of FIA/SCA
  Understand the physical behavior of FIA/SCA
  Through RTL/layout-level/post-silicon simulations and experiments, model the FIA/SCA effects under given input parameters
  For FIA, laser/optical fault-injections, clock/voltage glitching, and EM fault-injections have different mechanisms and modeling approaches
  Identify the cross-layer effects: how does the physical fault eventually impact the code execution?
Deliverables
  Model equations or look-up tables

## Slide 8: Task 1: FIA/SCA Modeling
Example: laser fault-injection modeling from layout info
  Laser effect can be modeled as extra current sources in SPICE simulations, then applied in dynamic IR drop simulations (result: build a connection between laser intensity per cell and cell’s accurate current demand)
  Cells’ current demand under laser impact will determine whether the fault can be injected
Example: clock/voltage glitch modeling from layout info
  Clock/voltage glitch causes timing violations across the sequential components
  Can be modeled as delay changes, i.e., converting fault to time
Repeat for all type of standard cells
Substitute impacted cells’ current
response with laser-impacted version
Voltage drop simulation on the layout

## Slide 9: Task 1: FIA/SCA Modeling
Example: laser fault-injection modeling from layout info
  Laser effect can be modeled as extra current sources in SPICE simulations, then applied in dynamic IR drop simulations (result: build a connection between laser intensity per cell and cell’s accurate current demand)
  Cells’ current demand under laser impact will determine whether the fault can be injected
Example: clock/voltage glitch modeling from layout info
  Clock/voltage glitch causes timing violations across the sequential components
  Can be modeled as delay changes, i.e., converting fault to time

## Slide 10: Task 2: Compiler Development
Test case and security properties
  Aims for C/C++ -> Assembly code compilation and hardening
  Plan to start with firmware, AES software, password checking, etc.
  Corresponding security properties acquired from existing standards and powerful attack scenarios
Modeling-compiler interface
  Modeling considers logical & physical info, thus, the outcome needs translation to be compiler-friendly
  Compiler must provide:
    A configurable “hardening level” input to determine the input (e.g., laser intensities) for FIA models
    A simple mechanism to determine target instructions (e.g., directly extract sensitive instructions from security properties; or through static code analysis.)
    Translation from target instructions to actual instances/area, which serves as final input for models
  Compiler must receive:
    Feedback from modeling in a compatible form of either 1) a threat level / a vulnerability ranking of inputted sensitive instances, or 2) a simple secure-or-not judgements from modeling under certain parameter inputs

## Slide 11: Task 2: Compiler Development
Hardening rules database
  Goal: address the physical faults during the compilation process
  Review existing hardening approaches
  Utilize or imitate existing solutions in RISC-V GNU compiler
  Develop adaptive approach to apply countermeasures using the info (e.g., vulnerability ranking) given by modeling output
Deliverables
  Encapsulated implementation of hardening compiler
  Proper documentations
Compile
Harden
What happened?
Faults modifying/bypassing the conditional jump will now directly lead to a password-checking failure

## Slide 12: Task 3: Evaluation
Technical Approach
  Execute hardened codes on FPGA/ASIC
  Perform FIA/SCA vulnerability analysis
  Evaluate the hardened code’s resistance, root-cause any issues, automate and improve the compilation flow
Deliverables
  FIA/SCA resistant code proven from physical modeling-assisted compilation
FICS lab houses state-of-the-art instruments and capabilities to perform cutting-edge research from device-to-system assurance, security, and integrity analysis.